Numerical Simulation Melting of Ice using OpenFOAM
Mr. Vignesh.S.P
M.E, College Of Engineeing Guindy, Anna University
Email : vikkypandiaraj@gmail.com

Abstract

This case study demonstrates the melting of ice. It’s a example of phase change process. The present case uses a multi-region approach to simulate the phase change process. The simulation is carried out in OpenFOAM v1906 using the solver chtMultiRegionFoam and the phase change is handled by solidficationMeltingSource source term. The geometry is a 2-D circle and the flow is laminar and transient. The volume fraction of melting water is obtained from the simulation
Problem Statement
The 2D geometry has a 30mm OD and 5mm thickness copper pipe, ice is present in the inner side of the pipe. The outer walls of the copper pipe are maintained at a constant temperature of 25o C. The 2D geometry generated by blocks for hexahedral mesh generation using Salome-Meca is given in the figure below